## Slide 1
Bluetooth Connection Notes:
169… IP Address
Max Bluetooth Connections:
  5 to Mac
  1 to PC
WiFi Connection notes:
Private IP Address (10.0…)
LED on the WiFi dongle shows network connection
Can be configured to automatically connect to a network
Can connect via telnet (requires installation) or ssh
Canakit WiFi Dongle

## Slide 2: Install Telnet
Install on EV3
Updates the package list
  sudo apt-get update
Install Telnet package
  sudo apt-get install telnetd
Install & Connect on Mac
Use Homebrew to install telnet
  brew install telnet
Connect with Telnet
  telnet -l robot <ip address>
  Password: maker
Using Telnet in Python
Telnet is insecure, but the EV3s have private IP addresses

## Slide 3
Wireless Network
Hardware
Wireless Network
Programming
EV3s Running EV3Dev with CanaKit WiFi Dongles
MacBook
Mac publishes local webserver
Mac sends commands to terminal from local webserver
Mac sends python3 commands to EV3 via telnet from terminal
EV3s connect to the wireless network on startup
User Inputs
Open webserver & enter commands

## Slide 4
Hardware
Wireless Network
Programming
EV3s Running EV3Dev with CanaKit WiFi Dongles
Raspberry Pi
Computer
RasPi reads IP addresses on the network and identifies EV3s*
RasPi publishes router level webserver
Computer sends commands via router level webserver
RasPi sends python3 commands to EV3 via telnet based on inputs to webserver
Wireless Network
EV3s connect to the wireless network on startup
User Inputs
Open webserver, select EV3*, & enter commands
*Working on python script to read IP addresses
SSH
Telnet

## Slide 5
Webserver Demo
EV3 Setup
  Configure EV3s to automatically connect to the wireless network
Raspi Setup
  Connect to wireless network
  Run WebserverDemoRasPi.py using python3 (can run on startup)
MacBook Setup
  Once the connection between the EV3 & RasPi is initiated and the webserver is created, navigate to <raspi IP>:8000
*Working on adding a slider bar for controlling speed

## Slide 6
EV3s Running EV3Dev with CanaKit WiFi Dongles
Intel Stick &
10.1" IPS Display Panel
Tufts Wireless
Hardware
Wireless Network
Programming Task
Student Computers
Telnet
Serve Webpage to control EVs
Read EV3 IP Addresses

## Slide 7
EV3s Running EV3Dev with CanaKit WiFi Dongles
Intel Stick &
10.1" IPS Display Panel
Local Area Network
Read EV3 IP Addresses
Hardware
Wireless Network
Programming Task
Student Computers
Verizon 4G Jetpack
Serve Webpage to control EVs
Broadcast LAN
Internet
Telnet

## Slide 8
EV3s Running EV3Dev with CanaKit WiFi Dongles
Local Area Network
Hardware
Wireless Network
Programming Task
Student Computers
Verizon 4G Jetpack
Serve Webpage to control EVs
Read EV3 IP Addresses
Intel Stick &
10.1" IPS Display Panel
Broadcast LAN
*
*Router may be needed for LAN
Internet
Telnet

## Slide 9
EV3s Running EV3Dev with CanaKit WiFi Dongles
Local Area Network
Hardware
Wireless Network
Programming Task
Student Computers
Verizon 4G Jetpack
Internet
Serve Webpage to control EVs
Read EV3 IP Addresses
Intel Stick &
10.1" IPS Display Panel
Broadcast LAN
*
*Router may be needed for LAN
Telnet